## Slide 1: PDM/PLM
15.10.2014
Kaur Jaakma

## Slide 2: Abbreviation
PDM
  Product Data Management
    Tuotetiedonhallinta
PLM
  Product Lifecycle Management
    Tuotteen elinkaaren hallinta
  Includes PDM
  Sometimes used as synonym
DMS
  Document Management System

## Slide 3: Product Data Management

## Slide 4: History
Late 1980s : Growing volumes of design files generated by CAD
  First custom EDM (Engineering Data Management) system appears.
  Soon commercial software renamed PDM (Product Data Management).
  Main functions: Incremental saving + versioning

## Slide 5: Evolution in PDM
Lots of CAD
  Data management functionalities
Lots of DESIGNER
  Need to support Concurrent Engineering (CE)
Switch from CAD as engineering artifact to CAD as official document
  Support for Bill of Materials (BOM) and integration with Enterprise Resource Planning (ERP)

## Slide 6: Reasons to Have PDM
Simultaneous design
  Who has the right version?
Several office locations
  Data in one place
Subcontractors
  Can share their files
Harmonize design process
  Encourage to use certain workflow and methods

## Slide 7: Core Functions
Data Storage
  Uses systematic way to store product related data
  Product, Project, Library…
Search
  Using search rules to find needed data
Access Control
  Who, where, what can do?
Change Management
  ”Where used” quarry
  What changed and why?

## Slide 8: Architecture of PDM

## Slide 9: Change Management

## Slide 10: Core Functions
Object handling
  Check-in/check-out mechanism
Version control
  Concurrent design
Data Lifecycle
  In design / production / maintenance
  Depending on company’s policies and data type
Data workflow
  Series of actions that must be taken upon change in the lifecycle status of the data

## Slide 11: Object Handling
Check-in
  Puts object into system
  New version
Check-out
  Loads data from system
  User have right to change object
  Locks from other users (read-only)
  Version not changed
    If canceled, nothing changes

## Slide 12: Version Control
Normally in X.Y format
X is revision
  Main version
  For ex. new part to assembly
Y is version
  Check-in creates new version
  For ex. part location changed
Depended on company policies
1.2
1.2+
Check-out
Check-in
1.3
1.2

## Slide 13: Data Lifecycle and Workflow Example

## Slide 14: Core Functions
Product structure management and maintenance
  Information that resemble the product structure, which consists of items hierarchically connected together
  Assembly’s model tree and custom folders
Configuration management
  Varying the physical properties of similar products and switching interchangeable assemblages or components. Configuration management allows products to be customized according to customer wishes
  CAD’s family table!

## Slide 15: Product Structure

## Slide 16: Object Relationships

## Slide 17: Version Control in PTC Creo
No overwriting
  New version with every save
  Simple offline version control system
  Can set privacy settings to files
Works with almost every file format
  prt.#, asm.#, sec.#, txt.#
Can be connected to PDM system

## Slide 18: Product Lifecycle Management

## Slide 19: PLM is NOT a Software!
Product lifecycle management does not refer to any individual computer software or method. It is a wide functional totality; a concept and set of systematic methods that attempts to control the product information.
However, in practice, PLM is carried out almost without exception with the help of different information processing systems

## Slide 20: What Is PLM? One Definition
“The core of product lifecycle management is the creation, preservation and storage of information relating to the company’s products and activities, in order to ensure the fast, easy and trouble-free finding, refining, distribution and reutilization of the data required for daily operations.”
                Sääksvuori & Immonen. 2008. Product Lifecycle Management.

## Slide 21: What Is PLM?
PLM is a holistic business concept
  Items and documents
  BOM’s
  Environmental component information
  Quality standards
  Engineering requirements
  Change orders
  Manufacturing procedures
  Product performance information
  Component suppliers
  Workflows (company’s internal procedure)
  Project control
  Etc.

## Slide 22: Requirements Management

## Slide 23: What Is PLM?
Modern PLM system helps standardize, automate, and speed up operations.
Web based systems enable companies easily to connect their globally dispersed facilities with each other and with outside organizations such as suppliers, partners, and even customers.
PLM is a collaborative backbone allowing people throughout extended enterprises to work together more effectively.

## Slide 24: PLM Functions

## Slide 25: Example: Siemens Teamcenter

## Slide 26: Another Example: PTC Windchill

## Slide 27: Final Remark about PLM
PLM is wide concept, related with:
  Engineering data management
  Enterprise processes
  Business and marketing of the product
Companies tends to deploy the PDM system provided by the same vendor of the CAD software
Other PLM functionalities are usually provided by specialized software
Integrating different specialized software is often complicated an expensive

## Slide 28: Similar Concepts

## Slide 29: Document Management Systems
Tracking and storing documents
  Word-, Excel-, PDF- etc. files
Like PDM but for non-CAD files
  Data storing
  Searching & indexing
  Data locks
  Versioning
  Collaboration
  Etc.

## Slide 30: Simulation Data/Lifecycle Management
Data management system for handling simulation data
  Very large objects
  Result files
  Simulation models
  Scripts
  Etc.
Layer to run simulations
  Querying
  Dedicated simulation server(s)
Should be part of commercial PLM

## Slide 31: Building Information Management
Used in civil engineering
Similar to PDM
Project based
Unique products

## Slide 32: Concurrent Versioning System
Used in computer engineering
  More weight on parallel working
  Can change same file(s)

## Slide 33: Vendors & Software

## Slide 34: Some Commercial PDM/PLM

## Slide 35: MS SharePoint
Document Management System (DMS) from Microsoft
Integration to Office tools
  Web usage
Possibility to expand
  SDM system plausible based on it
PTC ProductPoint
  Until the release of Windchill 10
  Based on SharePoint technology

## Slide 36: References (Pictures)
http://communities.ptc.com/servlet/JiveServlet/showImage/38-1748-23896/Layout+of+the+Windows.jpg
http://communities.ptc.com/servlet/JiveServlet/showImage/38-2227-30215/View+CAD+structure+directly+in+FlexPLM.png
http://communities.ptc.com/servlet/JiveServlet/downloadImage/38-2227-30209/Easily+view+interconnected+product+information+with+the+Relationship+Explorer.png
http://www.aras.com/plm-images/documents/slides/500x350-aras-plm-next-gen-req-mgt.png
http://www.ayokasystems.com/wp-content/uploads/siemens-550x280.jpg
https://encrypted-tbn3.gstatic.com/images?q=tbn:ANd9GcTaPHlkNTd1Ep-PNh7vx5Xnym2gFAGeZdpulKj1m0iiPC8M1o_Y
http://wildeanalysis.co.uk/system/photos/657/preview/ansys-ekm.jpg?1271444143
http://www.dowcotech.com/imgs/test/bim-steel.jpg
http://media.developeriq.in/media__/images/v_c2_24_07_09.gif
http://www.shorzinternational.com/contents/images/products/PDSDL.jpg